Statement of Work

for

Might Augmenting Exoskeleton (MAX)

# SCOPE

INTRODUCTION

The objective of this program is to evaluate and design a body-amplifying exoskeleton which will augment the effectiveness of a single infantryman. With the use of a stored energy tendon attached to a leveraged articulated frame, a soldier will be empowered to carry heavy loads over distance, quickly and efficiently. At the conclusion of the program, a rough demonstration prototype, along with documented research, will be delivered to DARPA.

TECHNICAL SCOPE

This program will define and implement a stored energy device. Using the weight of a soldier’s stride, the system will absorb and then rebound the soldier, propelling him to speed with minimal increased physical effort. This work will be conducted in two tasks: (1) a viable Stored Energy Tendon (SET) will be developed and tested (Task 1 – SET Development), and (2) application of the SET onto an articulated lightweight exoskeleton (Task 2 -Technology Application Development).

## TASK 1 – SET Development

## In this task, a single (mono) SET will be developed and constructed to absorb the specified weight and to release energy in a controlled manner. Considerations toward durability and repeatability will be made to ensure reliable performance in the field. A breadboard testing system will be assembled and evaluated.

## TASK 2 – Technology Application Development

This task will take the SET developed and validated in Task 1 and apply it to a lightweight structure that can be worn. An optimal geometry will be developed to provide for maximum flexibility and performance, as well as to work with a human’s natural running gait. Quick entry and release mechanisms will be developed at this time.

PROGRAM DESCRIPTION

# TASK I – SET Construction

#### Phase 1

### Expanding Current Capabilities

Because this exploratory process relies on the frequent use of costly fabrication methods, we are expanding our current prototyping capabilities to incorporate in-house composite spring lamination.  We are also contracting with a full-time composite fabricator.

## Research

Research will commence encompassing related fields of study including: a materials study, human and animal biophysics studies (focusing on running gait). Partnership with experts in related fields will help focus the effort. This will lay the groundwork for development of a SET that meets the requirements for the application.

## Development

Using the research and fabrication capabilities, a demonstration of a subset of the SPS will be constructed.

## Deliverable

1 Demonstration of a Subset of the SPS

## Phase  2

## Development

Construction will focus on a single (mono) SET.  This will be in the form of Super Pogo Stick (SPS).  We will focus on the composite lamination needed for the optimal spring rate.  The goal is to attain and control the 7-foot loft (hop) needed for high speed travel.  A breadboard will be constructed to evaluate the different iterations. Design issues will address the reliability and weight of the SET.  Once the system has been validated, the program will advance to the next phase.

Deliverables

1 working full-scale SPS

Animation used in development

Presentation Preparation

# TASK II – Technology Application

Applying the research in Task I, work will commence by developing a double (pair) SET incorporated onto an exoskeleton. Beginning with sketches and scaled models, the geometry will be finalized and evaluated.  Working drawings (orthographic) will then facilitate the construction of a full-scale demonstration prototype. Other design goals are:

- To address a quick entry and release.

- To develop mechanical joints that are robust. Provisions for repairing device in the field will be examined.

Deliverable

- Presentation material – as required

- Technical reports – as required

- Hardware documentation

- 1 Rough demonstration prototype

PROGRAM ADMINISTRATION

Next Planet will perform as a subcontractor to Mindtel.  Next Planet will be responsible for the above deliverables.

Outline Schedule